## Slide 1: Introduction To Application Development using OPC UA Libraries
What is OPC?
Benefits of OPC
Types of OPC technologies
Developing application to communicate with Siemens S7-PLC with OPC UA libraries

## Slide 2: What is OPC?
The acronym “OPC” stands for “OLE (Object Linking and Embedding) for Process Control”. OLE is based on the Windows COM (Component Object Model) standard.
OPC is a software interface interoperability standard that allows secure and reliable exchange of data between computer programs and industrial hardware devices. It is platform-independent and ensures the continuous flow of information across multiple vendor devices.
OPC standard is implemented in server/client pairs. The OPC server is a program that translates the hardware communication protocol used by a PLC into the OPC protocol. The OPC client software is a program that connects to the hardware, such as an HMI. The OPC client communicates with the OPC server to receive data or send commands to the hardware.

## Slide 3: Benefits of using OPC
Reduced load on the hardware device.
Increased scalability of the system.
Because of OPC server, client applications need not know anything about hardware protocol details.
Though device need not serve multiple clients, So Increased life for the device.
Interoperability (Unix/Linux and Windows – both platforms are supported by OPC)
Standardization

## Slide 4: Types Of OPC Technologies
These are the two popular OPC technologies that are used in modern industries:
OPC DA
OPC UA
OPC DA (Data Access Protocol):
It is s the most basic protocol of OPC. The representation of the data for DA is as follows: first the Value i.e. the data itself along with Name comes, and to that other information comes along with it such as Timestamp that provides the exact time when the value was read.
As OPC DA comes under OPC classic model, it supports DCOM communication for connecting the client and server, where DCOM is dependent on the operating system and supports only Window OS.
OPC DA allows to access only the current data and is incapable to generate alarms
One of the limitations of OPC DA is its inadequate security, as in today’s world security is the major issue because systems are more frequently attacked by some sophisticated viruses and malware
One of the applications of OPC DA is in factory automation for the communication from DCS and PLC to Management Information System.

## Slide 5
OPC UA:
It is a cross-platform protocol and that’s why it does not depend on any particular operating system or programming language. The architecture of OPC UA is service-oriented
Security provided by OPC UA is robust with Certificates which is not available in OPC DA
OPC UA do not rely on DCOM communication for connecting client and server, thus it is a platform or OS independent and it supports platform such as Linux (Java), Apple, or Windows.
OPC UA supports features like historical events, multiple hierarchies and provides methods and programs

## Slide 6
Developing Application Using OPC UA libraries